## Slide 1: Bluetooth at Shure
A Brief Brief by Josh Heise
Notes: Use this for Pro Audio Segments

## Slide 2: Confidentiality Reminder
This is secret stuff! Don’t tell anyone!

## Slide 3: Introduction
Bluetooth Classic
  5.0 Announced, not really on the market
  2Mbps
  Most hardware is on 4.0
  2.4Ghz
  Point to Point (One sink, one source)
Bluetooth Low Energy
  125Kbps
  Can network
  Many to many (mesh)

## Slide 4: How Do We Use It
Bluetooth Low-Energy
  Chronos
  MXA
  Taishin
Bluetooth Classic
  Listening
    TWS
    BT1
  Motiv

## Slide 5: Bluetooth Classic with Audio
Packages information
Streams to device
Unpacks information
Plays it back
A2DP (Advanced Audio Distribution Profile)

## Slide 6: Audio Profiles
A2DP for audio streaming
  Codecs
    MP3, SBC (audio sub-band codec), AAC, aptX, aptxHD
AVRCP (Audio/Video Remote Control Profile)
HSP (Headest)
HFP (Hands-Free Phone)
Source vs Sink

## Slide 7: THE REAL REASON WE’RE HERE
HARDWARE
  CSR8675 (for listening)
  Modules (BlueGiGa, BlueCreation)
  All-in-one solutions
Testing
  Audio Precision
  Proprietary IDE

## Slide 8: How Are We Better
Earphones
  Duh.
DSP
  120Mhz, 24-bit core, 32-bit instruction word, 12K x 32-bit program RAM
  External flash available
Antenna
  Current products have chip antennas
  Custom antennas coming soon

## Slide 9: Where to next?
True Wireless Stereo
Firmware Update
Listening App
Expanding Markets